Manual of Users

Model No.: Multi11

Chapter 1 Introduction

Chapter 2. Installation

1. Raise the screen slowly.

2. Install 2 hand holders on both sides

3. Connect the 2 handpieces. There are labels you can see, so you can know which handpiece to connect onto which socket.

3.1 How to connect.

3.1.1 Press down the 2 buttons firstly.

There are two buttons on both above and below of each handpiece. The two buttons may be in the upspring or press-down state. Before connect it onto the machine, it must be in the press-down state. So press down the 2 buttons firstly.

3.1.2 Connect it in the right direction.

There are two parts of the connectors: machine part and handpiece part. Please look at the following pictures. A1 connects to B1, and A2 connects to B2. It cannot plug if connecting A1 to B2.

3.1.3 Use some power of your hands to plug it. When you plug one well, you can hear the click – the button springs and it locks. Then you can try to pull the handpiece connector slightly to check whether or not it locks well. Then hang up the two handpieces onto handpiece holders.

4. Water-in. Pure water or distilled water necessary.

4.1 First, remove the black plug on the back of the machine. After the water-in, you do not need put it back again.

The method to take down the two plugs is to 1) push in the blue outlet and 2) pull out the plug at the same time.

4.2 Press the button on the water-in-hole.

Insert the water pipe with plug and add water via funnel.

Add water until water runs from Water Overflow hole.

Press the button on the Water-In mouth, the water pipe pops out automatically.

Chapter 3 Operating for SHR system

1. Connect the power. Turn on the machine by the key switch. If the machine has nothing reacts, turn the Quick Stop.

You see System Loading…. Just wait for seconds

2. Then next screen. This screen saved for add customers logo. If no special requirements, there will be no logo here or the producer’s logo.

LOGO

3. Click the above screen, we are in:

Click SHR, we go to:

②Treatment interface

Click Handle cool levels into full levels (from gray  to ) and the sapphire becomes cold in 1 or 2 seconds.

Pulse width: how long a shot work on skin. 1~7ms adjustable

Frequency: how many shots in one second. 1~10Hz adjustable

Energy:

- when the frequency is 1hz/2hz/3hz/4hz, the energy is 1-50J adjustable

- when frequency is 5hz, energy is 1-35J adjustable

- when frequency is 6hz, energy is 1-30J adjustable

- when frequency is 7hz, energy is 1-25J adjustable

- when frequency is 8hz, energy is 1-20J adjustable

- when frequency is 9hz, energy is 1-15J adjustable

- when frequency is 10hz, energy is 1-10J adjustable

When to adjust pulse width or Frequency, you need click the figure into red color:

Then click  to increase it or  to decrease it. Then click the red figure into white color again, or other settings are not able to change.

When you test the machine, you can use pulse width 3ms, frequency 3hz and energy 5J. Then raise the settings slowly according to actual situation.

When settings are ready, press "Ready” button to trigger the treatment head and to charge the capacitances automatically.

Press the button in the handpiece and it shots.

When treatment finishes, press "Standby” button to turn off the head.

Status prompt window

When the machine is Standby, it shows. When click Ready, it shows .

It may change between  and  during fast shots. It is normal.

When the water cycling is bad, the machine alarms and it shows .

When water temperature is too high, the machine alarms and it shows .

Operation

1. Shave the hair

Daub ultrasonic Gel on the skin in 1-2mm thick.

Please pay attention the way of handle during the treatment.

- Smear gel on the skin about 2 to 3 mm thickness before treating.

- Start the machine, processing step by step and adjust the suitable parametre.

- While exerting light pressure, approximate the treatment head perpendicularly over the treatment area. Ensure both metal slices of the head touch the skin naturally at the same time during treatment, If only one side metal slice touch the skin, it can be easily burnt skin. See above picture (1)Then can press the red bottoms to treatment. Before the treatment head leave the skin, please loose the red buttom first then treatment head can be off the skin.

- When the skin is in red after operation, coat the cool gel till the red is die out. Do not wash with water.

- Principles adjusting of parameters.

| The white skin and lighter Skin | 1.Increase the power engery |
| --- | --- |
|  | 2.Decrease the pluse delay=(pluse interval) more cooling |
| The daker skin | 1. Decrease the power energy |
|  | 2. Increase the pulse delay ( allow more cooling) |
| The lighter the hair /pigments | 1.Increase the power engery |
|  | 2. Decrease the pluse delay= ( pluse interval) |
| The darker the hair/ pigment lesion | 1. Decrease the power engery |
|  | 2.Increase the pluse delay= (pluse interval) more cooling |
| Fine Blood Vessels ( vascular lesion) | 1.Increase the power engery |
|  | 2. Decrease the pluse delay= ( pluse interval) |
| Thick Blood vessels | 1. Decrease the power engery |
|  | 2. Increase the pluse delay= ( pluse interval)cool more |
| The smaller the target size / lesion ( vascular) | 1.Decrease pulse delay |
| The larger the target size/ lesion ( vascular) | 1. Increase pulse delay ( allow more cooling ) |
| Bony prominences (forehead, molar area, shin, bikini) | 1. Decrease the power energy |

Chapter 4 Operation for IPL system

From the following screen. Click IPL

We enter IPL treatment screen

Click any function, go to screen:

Introduction of the screen:

Settings Storage : to store a group of personalized parameters. 3 files in each application.

Pulse number : it is seepage force. More number, stronger seepage force.

Return: to the screen to select functions

Flash interval ：To adjust the discharge interval, the adjusting extension is 1~5S, you can touch different figure. It the interval time bewteen the two adjacent flashes if keep pressing the switch on the handle.

IPL energy adjustment: to adjust the output energy of the light head. The adjusting extension is from 1 to 50 J/cm2. It can be changed during your treatment through clicking “△or▽”, “△”means up while “▽”means down.

Contact cooling level: to adjust the amount of snowflake from the left to right

The first pulse width: to adjust the first pulse width, the pulse width is the single pulse which be used, otherwise the first pulse width is the pulse width while many pulses be used. The adjusting extension is from 1 to 10ms by 0.1ms step in.

The first pulse duration: to adjust the first pulse width

The first pulse interval: to adjust the stay time between the first pulse and the second pulse, the adjusting extension is from 1 to 100ms by 1ms steps in.

The second pulse duration: to adjust the second pulse width, it will not display when single pulse be used. The adjusting extension is from 1 to 10 ms by 0.1ms step in.

The second pulse interval: to adjust the stay time between the second pulse and the third pulse, it will not display when single pulse be used, the adjusting extension is from 1 to 100ms by 1ms steps in.

The third pulse duration: to adjust the pulse width between the third and the fourth, it will not display when the single pulse be used, the adjusting extension is from 1 to 5ms by 0.1ms step in.

The treatment parameter can be changed, and you can adjust the parameter on the pulse wave pattern. The folder should be clicked again for saving the parameter after you input the needed number. The number will not be changed if the number is too big.

Sketch map of the pulse inputting

Head of state: used to display the head of state, there is  light up and extinguished in two states; after the head is lighted up, the machine can enter into the state of charge. If five seconds later, the head without light, then return to the standby state;

State of charge: used to display the charging state, have charge and without charging two states, after the success of charge, the system can carry out treatment status.

Flash status: used to display luminous state, representative is light;

The current counter: used to display the current treatment of luminous times.

Chapter 5 Usage of Handle

IPL handpiece

How to use filter for the IPL handpiece:

| Standard spectra | Application areas |
| --- | --- |
| 430-1200nm | Acne removal |
| 530-1200nm | Vascular 、pigment、photo rejuvenation |
| 590-1200nm | Acne |
| 640-1200nm | Hair removal |

Choose a right filter and install it onto the handpiece

There are 2 grooves here. Just insert the filter in this direction as shown in the picture.

When all the settings are ready, click Ready. You can hear PA. And at the same time the light in the handpiece is on.

Chapter 6. Treatment

After adjust the suitable parameters, the treatment site is coated with a thin layer of coupling agent (such as cold gel), will head the handle guide light crystal alignment treatment site (paste can not tightly pressed on the skin), press the handle button switch to carry out treatment, every time before sending light, machines will issue a "beep" warning sound, and then immediately out of light, a light once per second. When long time treatment, the internal temperature overheating, which cannot light treatment,

Thus machine need cool about 10 minutes that do treatment.

Notice attention:

Recommend if condition is ok,you can use zero constant temperature block compress with the treatment area.

In removing zero temperature block within 3 seconds of the parts of the E light treatment, which can prevent E light energy for certain sensitive skin injury.

Shutdowns:

(1) Release of the handle switch

(2) The E light treatment handles is replace back

(3) The machine interface is switched to the interface 1.

(4) Turn off the key switch

(5) The total power cut off

Note: if the customer can’t accordance with normal operation, will have danger photon radiation.

Attention after operation

1、Prevent from solarization: As the solarization may spur the rebirth of melanin, in 30 days after operation, patient should apply suntan oil with SPF 15 or sun block, and hold parasol or wear sunbonnet at outdoor place.

2、Face-painting: Face-making is not recommended after

Photons operation. A few days after operation, patients are not allowed apply chemical cosmetic or powdery makeup while biological skin-protection products are better. If symptoms like red turgescence or effusion, patient should report to doctors immediately and stop face-paiting. Take some Vitamin C and Vitamin E will help the treatment.

According to the normal physiological circle of human body, patient should go on with the next treatment 3 weeks after the operation. A period of treatment includes 3-5 treatments. After a period of treatment, typical flaws of skin like solar speckle, age pigment will be removed, and at the same time the skin will be tender, glossy and elastic.

Attention: Due to the constitutional difference, some clients may get vesicles, pigment diposition, red turgescence and gore. So patient could apply ice pack to the affected part for 30 minutes. Face- making is forbidden until 5 days later.

Contraindication

Cancer patients, hypotensives and diabetes sufferers, or people

With scar, cut or infected skin, abnormal diathesis or

Hyper susceptibility patients and people with irregular incretion are forbidden to undergo the operation.

Maintaining and Service

The equipment is constituted by precise optics instrument or electronic instrument. The maintaining and service of the machine should agree with the general regulation of precise optics instrument

Or electronic instrument. Avoid knocking, extrusion and vibration in placing and using it. Check the surface of lens after every operation, if there are splashing objects on it, dab them away with lens paper or cotton sticker with absolute alcohol

Skin-test (Essential)

Skin test is essential before the treatment for the safety operation. The detail is as following:

- Skin test should be performed before the treatment for the client when the first time. The test patch should be under the ears or other skins not influencing the facial beauty.

- Clean the test patch with pure water and wash- milk; apply a layer of cold coupling gel at the test patch. Take the treatment handle from the

- Supporter, and direct the light guide to the test patch. Trigger 2-3 shots (1/3 area of the spot size overlapping the treatment site is permitted.), and wait for 2-3 minutes to examine the test patch:

- If lightly swelling and/ or reddening at the test patch appears several minutes later, continue the treatment with the same settings of energy level and pulse type.

- If no visible changes at the patch appear, continue the test with 2j/cm² higher energy level. Re-perform the test for several times until the above situation happens.

- If the skin show adverse effect or excessive reddening and/or swelling at the test patch just after shot, continue the test with lower energy level.

- For hair-removal with the Hair-removal treatment handle (630-1200nm wavelength):

- First, cut off the hair and leave only 1-2 mm. clean the test patch with pure water, and apply a layer of cold coupling gel at the test patch. Take the treatment handle from the supporter, and direct the light guide to the test patch. Trigger 2-3 shots (1/3 area of the spot size overlapping the treatment site is permitted.), and wait for 2-3 minutes to examine the test patch:

- If swelling and/or reddening around the hair follicles appear within a few minutes, continue the treatment with the same settings.

- If no visible changes appear around the follicles, continue the test with 2j/cm² higher energy level.

- If the skin shows adverse effect such as excessive reddening or swelling), lower the energy level.

Cautions

- All personnel including clientele must wear protective glasses when the system is in use

- If do skin-rejuvenating for all face, start the treatment from the ear-root, and spread to all face

- One time overlapping to the pathology site is allowed.

- Place the treatment handle perpendicular to the skin, apply minimal pressure and slightly touch the skin. The light guide should be in complete contact with the gel.

- Leave no blank site and overlapping 1/3 of the spot size is allowed.

- Better not shoot the light at upper eyelid

For Skin-rejuvenating: The System emits varied wavelength, intense pulse, and broad-spectrum photon-current. It can permeate the cuticle to the derma and take effect on the abnormal pigment and vessel such target tissues to break the abnormal pigment cells, close the abnormal blood vessels, stimulate the proliferation of collagen and improving the rearrangement of elastic fibers, finally achieving   the purpose of pigment removal and skin rejuvenation.

For Hair –removal: The system emits varied wavelength, broad spectrum and mild pulse light that can permeate the cuticle to derma of the skin. Utilizing the selective absorption elements, the light is absorbed by the pigment of the hair follicles. Through the optical & thermal effect generated and sourced from the light, it achieve the purpose of removing unexpected hair by rapid destroying of hair follicle tissues.

Chapter 7. post-treatment care

No exposure to sunlight

Clients should use highest factor sunscreen and protect the treated area from exposure to sunlight, sunbed or other artificial tanning for one month following treatment. Tanning after treatment sessions may enhance melanin regeneration, which may result in hyper-pigmentation

Free from always touching and pressing

Clients must do not press and scratch the treated area against infection

Makeup immediately after the treatment is not allowed for better curative-effect, advising no use of makeup for four to five days following treatment. The skin is sensitive during this period. Remove the makeup when swelling and reddening appearing at the treated site against infection and pigmentation. In the mean time advise client take some

Food

Advising not eat the hot and spicy food because the skin is sensitive during this period.

Other

Advise that improve other causes of disease, such as adjusting the endocrine situation by taking Chinese herb of medicine, taking few medicines that include VitC and Vit E. According to the normal physiological process, clients should take the next treatment 21 days later. The whole treatment needs 3-5 times.

Chapter 8. Technical Specifications

| SHR | Energy | 1-50J |
| --- | --- | --- |
|  | Wavelength | 640-950nm |
|  | Pulse duration | 1-7ms |
|  | Pulse | single |
|  | Pulse Repetition Rate | 1-10HZ |
| IPL | Energy | 1-50J |
|  | Pulse No | 1-6 |
|  | Pulse Duration | 1-10ms |
|  | Pulse No. | 1-6 |
|  | Wavelength | 430/530/590/640nm standard |
| Basic specifications | Controller: | 10.4” color touch LCD screen |
|  | Output power | 2500W |
|  | Program languages | English, Spanish, French, German, Italian, Polish, Japanese, Korean, Chinese |
|  | Cooling System | semiconductor+ air + water + cooling gel |
|  | Skin Cooling | ≤0-100C |
|  | Dimension of machine | 58X50X39cm |
|  | Dimension of package | 72X59X59cm |
|  | N.W. | 27kg |
|  | G.W. | 45kg |
|  | Voltage | 100V~240V |

# Text boxes

SHR connector

IPL handle

SHR handle

Key Switch

Quick stop switch

10.4’’ movable color touch screen

IPL connector

Water In and Water discharge  hole

Air switch

Power socket

Water overflow hole

Machine part

A2

A1

Handpiece part

B2

B1

2. pull out the plug

1. push in the blue outlet

Water-in-hole and water discharge hole

Water overflow hole

system Settings

6 settings memories

Pulse width

Frequency

Counter

Status notification

Return Key

Ready /standby

Contact cooling

SHR energy adjustment

Current treatment patterns

Ready /standby/

Head cooling temperature selection coolingtemperature selection

IPL energy adjustment

Return

Status notification

Therapy parameter set

Settings Storage

The third pulse width

The second pulse width

The first pulse

The first pulse width

The first pulse interval

The second pulse interval

Discharge interval

RF delay

Beijing Renguang Weiye Science & Technology Development Co. Ltd